ACTIONHL-700HD

FEATURE

1. 16:9 HIGH LIGHT LCD PANEL, RESOLUTION 1024*600

2. BRIGHTNESS WAVEFORM DISPLAY

3. FALSE COLOR

4.SAFETY MARKS/TALLY

- B&W, BLUE ONLY

- SDI 1/1.001

7. HDMI 1.4

8. 16 CHANNEL AUDIO METERS(DISPLAY 8 CHANNELS. SELECTABLE)

- SAFE MARKER, FRAME, SUBTITLE FRAME

- 4:3、16:9、LETTER BOX、OVERSCAN

11. KEY LOCK FEATURE

12. BUILT IN 3D-LUT(REC709、SMPTE、EBU)

13. SELF DEFINED 3D-LUT  H/V-DELAY

14.BATTERY CHECKING

15. HDMI TO SDI OUTPUT

16. SDI TO HDMI OUTPUT

17. SDI VIDEO WAVEFORM HISTOGRAM

18. IMAGE FLIP

19. ANAMORPHIC LENSES 1.3x 2.0x

20. STILL FRAME

Specification

| PANEL | SIZE | 7” |
| --- | --- | --- |
|  | RESOLUTION | 1024×RGB×600 |
|  | DOT PITCH | 0.15（H）×0.15（V）mm |
|  | ASPECT RATIO | 16:9 / 4:3 SWITCHABLE |
|  | BACK LIGHT | White LED |
|  | BRIGHTNESS（MAX） | 1000cd/m2 |
|  | CONTRAST（MAX） | 700:1 |
|  | Color depth | 8Bits（16.7M） |
|  | IMAGE PROCESSING | 10Bits |
|  | RESPONSE TIME | 10ms |
|  | VIEWING ANGLE | H170° / V170° |

| VIDEO IN | 3G/HD/SD-SDI | 1 x BNC |
| --- | --- | --- |
|  | HDMI | 1 x HDMI Type-A |

| VIDEO OUT | 3G/HD/SD-SDI | 1 x BNC |
| --- | --- | --- |
|  | HDMI | 1 x HDMI Type-A |

| AUDIO | SDIaudio demultiplexing | yes |
| --- | --- | --- |
|  | audio meters | 16 channels |
|  | headphone | yes |

| Operation requirement | Input voltage | 12V DC four pin XLR |
| --- | --- | --- |
|  | Power consumption | 25W |
|  | Working temperature | 0-40℃ |
|  | Store temperature | -20-70℃ |
|  | Store humidity | 0%-90% No condensation |

| Structure | Shell material | Aluminum profile |
| --- | --- | --- |
|  | Dimension（mm） | 195 x 116.2 x 24 |
|  | Weight | About 1.0KG |

HDMI INPUT FORMAT

| HDMI | 480p/60、480i/60、576i/50、576p/50、720p(50/60)、1080i(/50/60)、1080p(24/25/30/50/60)、4096*2160p/24、3840*2160p 24/25/30 |
| --- | --- |

HDMI OUTPUT FORMAT

| HDMI | 480p/60、480i/60、576i/50、576p/50、720p(50/60)、1080i(/50/60)、1080p(24/25/30/50/60) |
| --- | --- |

SDI INPUT/OUTPUT FORMAT

| 425M(3G-SDI) | 1080p(50/60) |
| --- | --- |
| 274M(HD) | 1080i(60/59.94/50) 1080p(30/29.97/25/24/24sF/23.98/23.98sF) |
| 296M(HD) | 720p(60/59.94/50/30/29/25/24/23.98) |
| 259M(SD) | 480/59.94i、576/50i |