TL-B1730HD

FEATURE

1.16:9 FULL HD 1920*1080 ,HIGH CONTRAST PANEL

2.THREE WAVEFORM DISPLAY，（BRIGHTNESS/VECTSCOPE/RGB）

3. SDI，DVI SIGNAL WAVEFORM MONITORING

4.FOCUS ASSISTANT(RED/GREEN/BLUE/YELLOW)

5.FALSE COLOR

6.TIME CODE（VITC/VTC）

7.SAFETY MARKS/TALLY/UMD

8.B&W，BLUE ONLY

9.SDI 1/1.001

10.HDCP 1.1

11.H/V-DELAY

12.16 CHANNEL AUDIO METERS

13.LOCK FEATURE

14.BATTERY CHECKING

15.EMBEDDED 3D-LUT（Rec709、SMPTE-C AND EBU）

16.F KEY USER-DEFINED

17.FREEZE FRAME

SPECIFICATION

| PANEL | SIZE | 17.3inch |
| --- | --- | --- |
|  | RESOLUTION | 1920×RGB×1080 |
|  | DOT PITCH | 0.199（H）×0.199（V）mm |
|  | ASPECT RATIO | 16:9 / 4:3 |
|  | BACK LIGHT | RGB LED |
|  | BRIGHTNESS（MAX） | 350cd/m2 |
|  | CONTRAST（MAX） | 800:1 |
|  | Color depth | 10Bits(1.073G colors) |
|  | IMAGE PROCESSING | 10Bits |
|  | RESPONSE TIME | 3ms |
|  | VIEWING ANGLE | H178° / V178° |

| VIDEO IN | 3G/HD/SD-SDI | 2 x BNC |
| --- | --- | --- |
|  | COMPOSITE(CVBS) | 1 x BNC |
|  | COMPONENT | 1x 3 BNC |
|  | DVI | 1 x DVI-D |

| VIDEO OUT | 3G/HD/SD-SDI | 1 x BNC |
| --- | --- | --- |
|  | COMPOSITE | 1 x BNC |
|  | COMPONENT | 1x 3 BNC |

| AUDIO | audio demultiplexing | Yes |
| --- | --- | --- |
|  | audio meters | 16 channels |
|  | Speakers | 2x8Ω/2W |
|  | headset | yes |

| Operation requirement | Input voltage | DC 12V |
| --- | --- | --- |
|  | Power consumption | 25W |
|  | Working temperature | 0-40℃ |
|  | Store temperature | -20-60℃ |
|  | Store humidity | 0%-90% no condensation |

| Structure | Shell material | Cold-rolled steel |
| --- | --- | --- |
|  | Dimension（mm） | 451x281x44.6 |
|  | Weight | Around 6Kg |
|  | Fixing method | Desktop /Rackmount orVESA |
|  | Desktop and rack mount kits | available |

CVBS INPUT FORMAT

| CVBS | NTSC、PAL |
| --- | --- |

DVI-I input formats

| DVI-A | VGA(640*480)、SVGA（800*600）、XGA（1024*768）、WXGA（1280*768/1280*800）、SXGA（1280*1024）、SXGA+（1440*1050）、WSXGA（1680*1050）、UXGA（1600*1200）、WUXGA（1920*1200） |
| --- | --- |
| DVI-D | 480p/60、480i/60、576i/50、576p/50、720p(50/60)、1080i(/50/60)、1080p(24/25/30/50/60) |

COMPONENT input formats

| YPBPR | 480p/60、480i/60、576i/50、576p/50、720p(50/60)、1080i(/50/60)、1080p(24/25/30/50/60) |
| --- | --- |

SDI input formats

| 425M(3G-SDI) | 1080p(50/60) |
| --- | --- |
| 274M(HD) | 1080i(60/59.94/50) 1080p(30/29.97/25/24/24sF/23.98/23.98sF) |
| 296M(HD) | 720p(60/59.94/50/30/29/25/24/23.98) |
| 259M(SD) | 480/59.94i、576/50i |

Standard Accessories

|  | TL-B1730HD |
| --- | --- |
| AC-DC adapter | 1 |
| AC power cable | 1 |
| SDI cable | 1 |
| DVI to HDMI adapte | 1 |
| Fix nut | 4 |