TL-D3100K

| panel specification | Size | 31.1 inch |
| --- | --- | --- |
|  | Resolution | 4096×RGB×2160 |
|  | Dot pitch | 0.1704（H）×0.1704（V）mm |
|  | Aspect ratio | 16:9 / 4:3 switchable |
|  | Back light | WHITE LED |
|  | Brightness（MAX） | 350cd/m2 |
|  | Contrast（MAX） | 1450:1 |
|  | Color depth | 10Bits(1.073G) |
|  | Image processing | 10Bits |
|  | Response time | 9ms |
|  | Viewing angle | H178° / V178° |

| Video in | 3G-SDI | BNC x 4 |
| --- | --- | --- |
|  | HDMI 1.3 | Type A x 4 |
|  | HDMI 1.4 | Type A x 1 |

| video out | 3G -SDI | BNC x 4 |
| --- | --- | --- |

| Audio | Audio demultiplexing | support |
| --- | --- | --- |
|  | Audio meter | 8 lines |
|  | Embedded speaker | 2 lines x8Ω/5W |
|  | Headphone | support |

| HDMI | 480p/60、480i/60、576i/50、576p/50、720p(50/60)、1080i(/50/60)、1080p(24/25/30/50/60)、2160/30p |
| --- | --- |

| Color modes | REC-709、DCI-P3、REC-2020 |
| --- | --- |
| 4K-SDI | Square Division、2 Sample Interleave 3840*2160/24p/psf /25p/30p/50p/60p 4096*2160/24p/psf/25p/30p/50p/60p |
| 3G-SDI | 1080p(50/60) |
| HD-SDI | 1080i(60/59.94/50)1080p(30/29.97/25/24/24sF/23.98/23.98sF) 720p(60/59.94/50/30/29/25/24/23.98) |
| SD-SDI | 480/59.94i、576/50i |

| Working environment | Input voltage | AC 100 V-240 V、50 Hz/60 Hz |
| --- | --- | --- |
|  | Power(MAX) | AC:0.5-1.7A |
|  | Working temperature | 0-40 ℃ |
|  | Store temperature | -20-60 ℃ |
|  | Store humidity | 0%-90% no condensation |

| Structure | Case material | Aluminium |
| --- | --- | --- |
|  | Dimension（mm） | L742.4×H458.8×D81mm （monitor unit） |
|  | Weight | around 13.3KG |
|  | Fixing mode | desktop or VESA |
|  | VESA hole | 200*200mm |