# TL-P890YHD

FEATURE

1. 1920x1200 Native Resolution（IPS Technology）

2. Luminance waveform in SDI mode.

3. Grade & Step false color

4. Peaking Focus

5. Safety marker / Subtitle marker / TALLY / Static UMD

6. Black & white, blue, mono color switch

7. Compatible with SDI1/1.001 fps

8. HDCP 1.1 / HDMI 1.3

9. H/V Delay

10. Audio meter in 16 channels (Simultaneous display 8 channels)

11. 4:3 / 16:9 / Letter Box / Over Scan

12. Safety lock

13. Built-in 3D-LUT (REC709, SMPTE-C, EBU)

14. Fast keys (custom setting)

15. On display battery meter

16. Static-frame

SPECIFICATION

| PANEL | SIZE | 8.9” |
| --- | --- | --- |
|  | RESOLUTION | 1920×RGB×1200 |
|  | DOT PITCH | 0.09975（H）×0.09975（V）mm |
|  | ASPECT RATIO | 16:9 / 4:3 |
|  | BACK LIGHT | WLED |
|  | BRIGHTNESS（MAX） | 500cd/m2 |
|  | CONTRAST（MAX） | 800:1 |
|  | Color depth | 8Bits(16.7M colors) |
|  | IMAGE PROCESSING | 10Bits |
|  | RESPONSE TIME | 10ms |
|  | VIEWING ANGLE | H170° / V170° |

| VIDEO IN | 3G/HD/SD-SDI | 2 x 2 x BNC |
| --- | --- | --- |
|  | COMPOSITE(CVBS) | 2 x 1 x BNC |
|  | COMPONENT | 2 x 1x 3 BNC |
|  | HDMI | 2 x 1x HDMI Type-A |

| VIDEO OUT | 3G/HD/SD-SDI | 2 x 1 x BNC |
| --- | --- | --- |
|  | COMPOSITE | 2 x 1 x BNC |

| AUDIO | audio demultiplexing | Yes |
| --- | --- | --- |
|  | audio meters | 16 channels |
|  | Speakers | Stereo 1x8Ω/1W |
|  | headset | yes |

| Operation requirement | Input voltage | DC 12V |
| --- | --- | --- |
|  | Power consumption | 15W |
|  | Working temperature | 0-40℃ |
|  | Store temperature | -20-70℃ |
|  | Store humidity | 0%-90% no condensation |

| Structure | Shell material | Aluminum profile |
| --- | --- | --- |
|  | Dimension（mm） | L222 x H177 x D58.5mm |
|  | Weight | Around 1.5Kg |