VF-701HDA

FEATURE

1.High Contrast LCD Panel （800：1）

2.High Resolution LCD Panel（1280×800）

3.Wide View Angle（H178°/V178°）

4.High Brightness、adjustable rear-mounted TALLY Light

5.External TALLY signal input terminal post

6.Assisting Focus Function

7.Linear zoom trigger （patent technology）

8.Out of range signal detect function

9.Monochrom（BLUE ONLY）

10.Safety mark，Center mark，Title frame

11.4：3/16：9、Letter box、Overscan、full screen

12.Safety Lock Function

13.F key Self-defining function F

14.Super-long sunhood

SPECIFICATION

| PANEL | Screen Size | 7” |
| --- | --- | --- |
|  | Resolution | 1280（H）×800（V） |
|  | Dot Pitch | 0.117（H）×0.117（V）mm |
|  | Aspect Ratio | 16:9 / 4:3 Switchable |
|  | Brightness（MAX） | 400cd/m2 |
|  | Contrast（MAX） | 800:1 |
|  | Color Depth | 8Bits(16.7M Colors space ) |
|  | Image processor | 10Bits |
|  | Response Time | 12ms |
|  | Viewing Angle | H 178° / V 178° |

| VIDEO IN | VF | 20 pin VF Cable |
| --- | --- | --- |

| Operation requirement | Input Voltage | DC 12V Standard 4 pin XLR |
| --- | --- | --- |
|  | Power Consumption(MAX) | 11W |
|  | Working Temperature | 0-40℃ |
|  | Storage Temperature | -20-60℃ |
|  | Storage Humidity | 0%-90% Non-coagulation |

| Structure | Shell Materials | ABS engineering material |
| --- | --- | --- |
|  | Dimensions（unit：mm） | 207(w)X151(h)X60(d) |
|  | Weight | About 1Kg |
|  | Installation Device | Video Camera |

Standard Accessories

|  | VF-701HDA |
| --- | --- |
| Fixing screws | 2 |
| VF Main line | 1 |
| U bracket | 1 |
| FoldableSunhood | 1 |
| Linear zoom trigger | 1 |