AT-2151HD+

FEAUTURES: Metering function*, Built in 3D LUT, Luminance waveform,False color,  Peaking Focus, Zebra, Audio level meter, Safety Marker, Marker Scale, Mono-chrome switch, Over Scan, GPI Control, Battery indicator.

HDR:HLG( ITU-R BT.2100), PQ (SMPTE ST.PQ2084), 2.4HDR, S-Log3_HDR、Log-C_HDR

*Metering function: It can detect out of luminance range signals in the screen within one second and accurately display the specific location of out of range signals. Moreover, by adjusting the IRE range, the dynamic range and image tone of different cameras can be matched.

HIGHLIGHTS:

*High brightness: 2000cd/㎡

*It can cover 96% DCI-P3, supports Rec.2020.

*HDR Mode

SPECIFICATIONS:

| Size | 21.5 inch |
| --- | --- |
| Resolution | 1920(H)×1080(V) |
| Dot pitch | 0.247(H)×0.247(V)mm |
| Aspect ratio | 16:9 / 4:3 Switchable |
| Brightness | QD+Blue LED |
| Brightness(MAX) | 2000cd/m2 |
| Contrast (MAX) | 1000:1 |
| Color depth | 8Bits(16.7M Colors) |
| Image processing | 10Bits |
| Response time | 7ms |
| Viewing angle | L89 ° R89 ° U89 ° D89 ° |

| Video Input | 3G/HD/SD-SDI | BNC x 2 |
| --- | --- | --- |
|  | HDMI | HDMI 1.3 x 1 |
| Video Output | 3G/HD/SD-SDI | BNC x 1 |

| Audio | Audio demultiplexing | Yes |
| --- | --- | --- |
|  | Audio meters | 16 channels (Max.8 channels display) |
|  | Speakers | 2linesx8 Ohm/2W(Rear) |
|  | Headphone | 3.5mm |

| 3G-SDI | 1080p(50/60) |
| --- | --- |
| HD-SDI | 1080i(60/59.94/50)1080p(30/29.97/25/24/24sF/23.98/23.98sF) 720p(60/59.94/50/30/29/25/24/23.98) |
| SD-SDI | 480/59.94i、576/50i |
| HDMI | 480p/60、480i/60、576i/50、576p/50、720p/50/60、1080i/50/60、1080p/24/25/30/50/60 |

| Operation | Input voltage | DC 12V Standard 4 x Pin XLR |
| --- | --- | --- |
|  | Power consumption(MAX) | ≤55W |
|  | Working temperature | 0-40℃ |
|  | Store temperature | -20-60℃ |
|  | Store humidity | 0%-90% No Condensation |

| Structure | Shell Material | Aluminum Alloy |
| --- | --- | --- |
|  | Dimension (mm) | L514.8×H328×D40mm |
|  | Weight | Around 4.7kg |
|  | Installing Way | Desktop or VESA |
|  | Mounting Holes | 100*100mm |

Standard Accessories: AC-DC adaptor, power cable, detachable desktop holder

Optional Accessories: V mount battery plate, golden battery plate, HDMI Lock, VESA mount, SDI cable, Armor No1.Case